## Slide 1: More Clocks and Timers
Lecture #11

## Slide 2: MSP430F5529 Clock System
>> MSP430 Clock module is very capable, wide variety of clocking options under software control
>> Unified Clock System (UCS) --5 possible Clock sources
  XT1CLK = LF Crystal 32,768 Hz REF0CLK = Internal osc., 32768 Hz
  XT2CLK = 4MHz crystal
  DCOCLK = Internal Digitally Controlled Oscillator (frequency selectable) (can use LF and HF crystals as source)
  VLOCLK = Internal osc., ~10KHz
>> Provides 3 clock signals to CPU and peripherals (On Reset theyDEFAULT to the following... KNOW THESE!)
  ACLK= Auxillary Clock = XT1CLK = 32768 Hz
  MCLK= Master Clock (CPU) = DCOCLK = 32*XT1CLK = 1.048576 MHz
  SMCLK = Sub-main Clock = DCOCLK = 1.048576 MHz
>> Clock sources/speeds for CPU and peripherals are SOFTWARE selectable
  Controlled through 9 registers (see User's Guide!)

## Slide 3: TIMERS
>> Digital circuit block that counts clock ticks
>> Digital circuit that is separate from CPU
3.3 V
0 V
4-bit counter
clk
4-bit count
0000
0001
0010
0011
1111
0000
. . .

## Slide 4: TIMER - Modes
  Unidirectional mode (Up mode in MSP430) = Count from 0 to a programmer set maximum count
  = time between interrupts

## Slide 5: TIMER - Modes
  Continuous Mode = Counts from 0 to Full Count of timer (8, 12 or 16 bits)
  = time between interrupts

## Slide 6: TIMER - Modes
  Up/Down mode = Counts from 0 to selected Max Count then back to 0
  = time between interrupts
  >> Timers typically generate an Interrupts (to the CPU) at the transition back to 0

## Slide 7: Interrupts
Signal to the CPU from a peripheral or other external source
>> Typically either a request for service from the CPU or a notification that peripheral has something (data) for the CPU
>> CPU chooses to accept or ignore interrupts
  except Non-maskable Interrupts: Power Faults or Oscillator Faults
>> What will an interrupt from a timer mean?
  That a fixed amount of time has elapsed

## Slide 9: MSP430F5529 - General Purpose Timers
>> Timer B
  Used by Graphics Library
    7 Capture and Compare registers
    PWM used for Buzeer
>> Timer A0
  PWM
>> Timer A1
  PWM
  Used by LCD
>> Timer A2
  We will used for measuring time
  3 Capture and Compare registers

## Slide 10: MSP430F5529 - General Purpose Timers
>> Plus a Basic Timer (w/ Real-time clock features)
>> And a Watchdog Timer....
  When it's ON, the WDT must continually have its count reset within the program
  If the WDT is ON and its count gets to 0 it will reboot the MSP430!
  Which is why the first instruction in your main()should be
WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer

## Slide 11: MSP430F5529 - General Purpose Timers
>> Like the '430 Clock module, the Timers are highly (almost infinitely) configurable!
>> We will stick to the basics –they can be confusing enough!
  Add complexity ONLY when needed!

## Slide 12: MSP430F5529 - General Purpose Timers
>> Using Timers in Programs --What does the programmer need to do?
>> Select a Timer -- How about Timer A2???
  We'll use Timer A2 because on our lab boards the Timer A1 is used by the LCD and Timers B are already used by the buzzer.
>> Map desired behavior in to an operating mode (Up, Continuous, Up-Down)
  Usually use UP mode so we can control time interval by selecting
  Would choose UP/DOWN to extend the interrupt time to its maximum
>> Select Clock Source & Configure control register(s) appropriately
  Selected Clock frequency and MAX count determines time resolution
is loaded into TA2CCR0 register

## Slide 13: MSP430F5529 - General Purpose Timers
--Write Interrupt Service Routines (ISR) and enable interrupts
>> In C, you need implement ISR function and also do global interrupt enable
>> Later in main() you must enable interrupts…
// Example syntax for Timer A2 interrupt service routine
#pragma vector=TIMER2_A0_VECTOR
__interrupt void Timer_A2_ISR(void)
{
// Do something
. . .
}
// Using msp430.h definitions
_BIS_SR(GIE); // Global Interrupt enable

## Slide 14: Interrupt Service Routine
But how do you decide what the timer settings should be and what the ISR should do?
Example: Implement a stop watch that measures seconds and hundredths of seconds using TimerA2. (Example code posted)
First question, how will we measure the passage of 0.01 seconds?
  By counting clock ticks
How many clk ticks 0.01 sec?
  Depends

## Slide 15: Interrupt Service Routine
>> Clock on the right will count to MAX_CNT faster
>> We need to choose a clock source
  ACLK or SMCLK
  ACLK = 32768 Hz sec
  SMCLK = 1.048576 MHz sec
>> Only measuring 0.01 sec
  ACLK has more than enough resolution

## Slide 16: Initializing control registers
TA2CTL =
TA2CCR0 = 327; // 327+1 = 328 ACLK tics = ~1/100 seconds
TA2CCTL0 = CCIE; // TA2CCR0 interrupt enabled
TASSEL_1
+ ID_0
+ MC_1
Use ACLK
Divider=1
Up Mode
MAX_CNT
Enable interrupts

## Slide 18: Interrupt Service Routine
>> What will it mean when we get an interrupt from TimerA2? What should the ISR do?
  Nothing unless we also enable interrupts for the CPU within our program!
  _BIS_SR(GIE)
>> Each interrupt means that 327+1 clock ticks have elapsed = ~0.01 second using ACLK
>> TimerA2 ISR should count how many interrupts have occurred!
  Global variable timer is a count of the number of 0.01 second intervals that have elapsed
#pragma vector=TIMER2_A0_VECTOR
__interrupt void Timer_A2_ISR(void){
timer++;
}

## Slide 19: Interrupt Service Routine
>> What does the CPU do when it receives the interrupt (assuming interrupts are enabled) and between interrupts?
>> Arrival of INTERRUPT is Asynchronous to program execution
>> Never know when INT will occour
ISR
ISR
Flow of main program
Main

## Slide 20: Interrupt Service Routine
>> CPU finishes current assembly instruction then foes to ISR like it was a function call
>> After ISR complete, CPU resume execution where it left off!
unsigned int timer; // global timer count variable
while(1) // Forever loop of the stop watch{
. . .
chkBtns(); // check for button press
if(button1){
timer_on=0;
stoptimerA2(1); // reset timer
P1OUT =~BIT0; // turn LED off
}
if(button2){
timer_on=1;
runtimerA2(); // starts timer
P1OUT =~BIT0; // turn LED off
GrClearDisplay(&g_sContext);
}
if (timer_on)
if (timer%10==0) // update display every 1/10th sec
displayTime(timer);
} /* End while(1) loop */
INT occurs
INT occurs
INT occurs