## Slide 1: Getting to know the Hardware: The MSP430F5529 Architecture & Memory Map
Lecture #4-5

## Slide 2: Getting to know the MSP430 Hardware
In a Programming course – Typically its all about the code
  Read in data
  Manipulate data
  Output/Store data
>> Learn syntax of a high-level language & logical and algorithmic approaches to solving some (common) problems
>> Use a very high-level view of a computer

## Slide 3: Getting to know the MSP430 Hardware
Use constructs
  loops, arithmetic operations, searches, if-then-else, sorts, calculate
Software: Write function & syntax correctly and it will run
Use library functions for I/O read(), getchar(), send(), printf(), putchar() …
Computer
Keyboard
Monitor
Disc, I/O

## Slide 4: Getting to know the MSP430 Hardware
>> Developing SW for embedded systems requires much more in-depth knowledge of target microprocessor
  Need to understand architecture of the processor
  How & Where code and data are stored
  How much memory & what resources are available

## Slide 5: General Microprocessor System HW Architecture
CPU = Central Processing Unit = Core or brains of computer
  Executes program instructions
  Provides timing
  Controls/Directs operation of memory and peripherals
Memory = Stores binary information
  Under control of CPU (memory is DUMB!)
  2 main types
    Non-volatile -> ROM/FLASH = code Memory
    Volatile -> RAM = Data Memory
Peripherals = Everything that’s not memory
  Provide means of exchanging data with the I/O devices
  I/O Access is similar to Memory Access in Embedded Systems
    Memory Mapped Peripherals
CPU, Memory, Peripherals connected through
  data lines, address lines & control lines
Bus
  Multiple connections in parallel
CPU
Memory
Peripherals
(I/O devices, etc.)
Control lines
Address Bus
Data Bus

## Slide 6: General Purpose (PC-style) Computing Hardware/Software Hierarchy
Applications Office, Matlab
Operating System = User Interface Win 10, Linux, MacOS
System SW = Interface to HW (Hardware Abstraction Layer) Device Drivers, BIOS
HW Layer = CPU, MEM., Peripherals

## Slide 7: Embedded System Computing Hardware/Software Hierarchy
Everything gets “squashed” in an embedded system…
Application (singular!)
  Closely integrated with Hardware Layer
  I/O is Low Level
  Reads/Writes to pins of Microprocess
  Little or no wrapping of I/O functions (no printf(), etc.)
Applications
Operating System/OS
HW Layer = CPU, MEM., Peripherals

## Slide 8: Architectures
>> Most microprocessor/microcontrollers are use one of the following architectures
Von Nuemann (or IAS or Princeton) Architecture
-- first used for IAS Computer (~1952)
Harvard Architecture
-- first used by Harvard Mark I (~1944)

## Slide 9: Harvard Architecture
Separate Memory for Data and Instruction
Data and Instruction Fetch happens at the same time
  Single instruction cycle
More complicated and costlier development
CPU
Code Mem
Data Mem
Instr Addr
Code
Control
Data Addr
Data Bus
Control
Peripherals

## Slide 10: Von Neumann Architecture
Same Memory for Data and Instruction
Data and Instruction Fetch happens on different times
  2 instruction cycles
Easier and cheaper development
Used by most “general purpose” processors
MSP430 also uses this
CPU
Memory
(Code)
(Data)
Data Addr
Data Bus
Control
Peripherals

## Slide 11: MSP430F5529 – Functional Block Diagram
>> MSP 430 family contains over 100 versions of this CPU with various memory/ peripheral configurations
  --Really a “System on a Chip”
  MAB -> Memory Address Bus
  MDB -> Memory Data Bus
>> We'll be using MSP430F5529
  128 KB Flash memory > Code storage
  8 KB RAM (+2 KB RAM associated with USB) > Data storage
  LCD controller
  32-bit Hardware multiplier, Serial interfaces (UART), analog to-digital converter (ADC) and a slew of other peripherals
  Multiple timers, comparator, USB controller, DMA, general IO ports...

## Slide 13: Memory Organization
>> Memory = group of sequential locations where binary data is stored
  In MSP430, each memory location holds 1 byte
  Each byte has unique address which CPU uses to read to and write from that location (think “mailbox”)
  Multibyte data is stored Little Endian! (low byte, high byte)

## Slide 14: Memory Organization
Words are aligned with even addresses
  Low byte always stored at even address
Byte F3h is at address 02401h
Word F307h is at address 02400h
Address | Byte Value
… | …
02403h | 02h
02402h | 02h
02401h | F3h
02400h | 07h
… | …
Word = F307h
Addr = 02400h

## Slide 15: Volatile vs Non-volatile Memory
Non-Volatile
  Keeps contents when power removed or interrupted
FLASH
  128 KB = CODE memory (primarily!) = Non-volatile
  Fetch = retrieving of instruction from CODE (Flash) memory (automatic CPU function)
  Flash is writable under program control
    time required to write >> time required to read
    Must be erased in multi-byte segments (e.g 512 bytes)
Volatile
  Loses contents when power removed or interrupted
RAM
  8 KB (+2 KB) = DATA memory = Volatile
  Read and Write = retrieving or writing DATA to/from RAM (under programmer control)
  (MSP430F5529 –has a RAM retention low power mode)

## Slide 16: MSP430 is 16-bit microcontroller
>> 16-bit word size => 16-bit internal registers
>> 16-bit data bus
>> BUT MSP430x5xxx and '6xxx families have and extended 20-bit memory address bus to allow access to up to “1MB” of memory
>> Each bit in bus has its own electrical connection!
  Parallel bus
CPU
Register 0
Register 15
Memory
A19
A18
A0
D15
D14
D0
Address
Data

## Slide 17: Memory Size Conversion
>> 1 KB = 210 bytes = 1024 bytes
Also,
>> 210 bytes = 1024 bytes = 1 kilobinary = 1KiB = 1 kibibyte

## Slide 18: Memory Organization
>> RAM starts at 02400h, implemented in 2KB banks (sectors)
  Variables used during program execution are stored in RAM
>> Our 128 KB of Flash starts at 04400h and ends at 0243FFh.
  (Interrupt Vector Table is written within Flash)
>> Code is written to Flash when you program the chip from CCS starting at address
  04400h (by default, can give compiler directives specify other location)

## Slide 19: Internal Registers
>> There are sixteen 16-bit register inside CPU
  Registers R0 –R3 have dedicated functions
>> Registers R4 –R15 are user registers
  Like scratch pad for data values being used by current or recent instructions
  Retrieving an operand from a CPU register is much more efficient than reading it in from memory
  CCS compiler tries to maximize register use
(20-bits)
(20-bits)
(16-bits)
(16-bits)
Used by CPU to control program execution
    R0 = Program Counter
    R1 = Stack Pointer
    R2 = Status Register
    R3 = Constant Generator
Hold addresses -> 20-bits

## Slide 20: Peripherals
>>What's the deal with the addresses below 00FFFh assigned to peripherals?
  These addresses are associated with the Control and Data registers of the peripherals
  Allows for data to be read or written to I/O peripherals as if being read or written to memory
–They are what you use to do IO!!
>> Almost all computer programs require Input and produce Output...

## Slide 21: Consider this C code for a General-Purpose computer
#include <stdio.h>
void main(){
  charinKey = '-’; // declare variable named inKey
  // and initialize to ASCII '-'
  while (inKey != 'X'){
    /* get character from keyboard */
    inKey = getchar();
    /* display character entered on screen */
    putchar(inKey);
  }
}

## Slide 22: C code for a General-Purpose computer
How is the Input and Output handled? Is it just a simple bit of software?
>> getchar( )and putchar( ) are C functions and part of the stdio library
➔ Their function prototypes can be found in stdio.h
➔ Also their implementations are part of stdio library which is “included” during the build process (compilation and linking)
>> These “canned” software routines have Why embedded stuff is cool! Always been part of standard C because everybody using general purpose computers has needed to read characters from a keyboard and write to a monitor!
➔ Several computing “layers” below our simple little application a byte has been placed on the microprocessor’s data bus from the PORT attached to the keyboard…

## Slide 23: C code for a General-Purpose computer
Applications
Operating System = User Interface
System SW = Interface to HW (Hardware Abstraction Layer)
HW Layer = CPU, MEM., Peripherals
getchar( ) and putchar( ) = C Library functions
CPU
Keyboard
Monitor
Port A
Port B
Data Bus
Addr Bus
Byte must be “written” or “read” from voltages applied to or on the package pins of the CPU
Voltages -> Logic Levels 0 or 1